## Slide 1: Adapting Your Contest Strategies to the Rapidly Declining Solar Cycle 24
Two more years of declining solar activity
Then at least three years of solar minimum

## Slide 2: Two More Years of Declining Solar Activity Then Three+ Years of Solar Minimum

## Slide 3: What About Solar Cycle 25 ?? Precursors of a possibly weak Solar Cycle 25
Sunspot Number
Accurate Cycle 25 forecasting is not possible until about three years after solar minimum
Unusually weak solar polar magnetic field strengths
  field strengths should reach their peak between 2018 and 2020
    www.solen.info/solar/polarfields/polarfields.jpg
Unusually large numbers of spotless days
  possibly starting later this year or next year
Unusually quiet geomagnetic field from 2018 to 2020+
  reported by the A-index
Unusually late appearance of new Solar Cycle 25 sunspots
  new Solar Cycle 25 sun spots should appear by 2020
Unusually long solar minimum
  solar flux in the low 70s persisting after 2020

## Slide 4: Declining Solar Activity Since Cycle 22 Suggests a Weak Solar Cycle 25
Cycle 25?

## Slide 5: The Sun’s Polar Magnetic Field Strength A Reliable Precursor of Solar Cycle 25
Strong polar field strengths late in Solar Cycle 21
-200 uT Polar Field Strength +200 uT
Weak polar field strengths late in Solar Cycle 23
Cycle 25
www.solen.info/solar/polarfields/polar.html
Polar magnetic field strengths late in Cycle 24?

## Slide 6: 160 Meter Propagation During the Two Year Decline to Solar Minimum
Improving DX propagation
  stronger signals
  more reliable openings especially to Europe and Japan
  lower geomagnetic activity
    especially as we approach solar minimum in ~2020
    declining daytime D layer absorption before sunset and after sunrise
  declining nighttime E layer absorption
More crowded band conditions
  especially when there is no strong 40 meter propagation to Europe
Longer and more regular worldwide openings
  reliable openings to Europe, Mid-East & north Africa 2130-0830Z
  more frequent openings to JA at our sunrise ~1200-1230Z

## Slide 7: 80 Meter Propagation During the Two Year Decline to Solar Minimum
Improving DX propagation
  stronger signals
  more reliable openings especially to Europe and Japan
  lower geomagnetic activity
    especially as we approach solar minimum in ~2020
    declining daytime D layer absorption before sunset and after sunrise
  declining nighttime E layer absorption
More crowded band conditions
  especially when there is no strong 40 meter propagation to Europe
Longer and more regular worldwide openings
  continuous openings to Europe, Mid-East & north Africa 2100-0830Z
  regular openings to JA starting before sunrise ~1130-1300Z

## Slide 8: 40 Meter Propagation During the Two Year Decline to Solar Minimum
  Nearly 24 hour DX propagation during CQWW CW
  Europe, Mid-East, north Africa propagation
    activity QSYs to 40 meters earlier in the afternoon ~1930Z
    don’t miss the strong mid-afternoon European openings!
      beginning at about 1930Z to 2030Z (earlier in New England)
      propagation may fail several hours after our sunset at about 0100Z
    strong openings often resume at European sunrise: ~0600-0900Z
  Japan, Far East and Central Asia propagation
    brief direct path opening starting before JA sunset: 0800-0900Z
    weak skew path opening at ~ 240 degrees azimuth ~0900-1130Z
    the strongest opening from the east coast: ~1130-1300Z
      direct path strong signals for an hour or more
    strong long path signals at 150 degrees azimuth: 2130-2215Z
  VK/ZL and south Asia long path propagation 2100-2300Z
  south and central Asia long path propagation ~1200-1300Z

## Slide 9: 20 Meter Propagation During the Two Year Decline to Solar Minimum
  Usually closes well before midnight ~0300Z
    usually stays closed all night
  Europe, Mid-East, north Africa propagation
    from before our sunrise until mid afternoon ~1000-1900Z
      the opening may be delayed to until sunrise or later
    shorter openings than we’ve enjoyed in recent years
  Japan, Far East and central Asia propagation
    afternoon short path opening from 2130Z to about 0000Z
    morning short path opening from about 1300Z to about 1500Z
    significantly shorter openings than we’ve enjoyed in recent years
  Long path to VK/ZL and south Asia starting in mid-afternoon
    starting about 1900Z until our sunset
  Long path to south Asia begins about an hour after our sunrise
    starting about 1300Z until about 1500Z

## Slide 10: 15 Meter Propagation During the Two Year Decline to Solar Minimum
  Usually closes a few hours after our sunset ~0200Z
    always stays closed all night
  Europe, Mid-East, north Africa propagation
    from about our sunrise until mid-afternoon 1200Z to about 1800Z
    much shorter openings than we’ve enjoyed in recent years
  Japan, Far East and central Asia propagation
    afternoon short path opening from 2130 to about 0000Z
    morning long path opening from about 1300Z to about 1400Z
    polar opening to central Asia from about 1400 to about1600Z
    much shorter openings than we’ve enjoyed in recent years

## Slide 11: 10 Meter Propagation During the Two Year Decline to Solar Minimum
  Usually starts to open about an hour after our sunrise ~1300Z
  Usually closes a few hours after our sunset ~0000Z
    always stays closed all night
  Europe, Mid-East, north Africa propagation
    short path propagation becomes less frequent and much shorter
    weak signal skew paths (110-150 degrees) typically ~1400-1700Z
  Japan and Far East propagation
    short path propagation is extremely unusual
    morning long path starting at about 1300Z to about 1400Z
    evening skew paths (200-270 degrees) from ~2130Z to 2230Z

## Slide 12: DX Contest Strategies for the Two Year Decline to Solar Minimum
  Improve your low band antennas this summer!
  Start the contest on 40 meters
    the strong European opening could end after just a few hours
  Capitalize on improving 160 and 80M propagation 0200-0830Z
    mainly when 40 meters is not strongly open to Europe
  Look for a strong European opening on 40 meters 0600-0900Z
  160, 80 and 40 meter openings to VK, ZL, JA 0900-1230Z
  Look for the start of the 20M European opening 1000-1200Z
  Look for the start of the 15M European opening 1200-1400Z
  Check 10 meters frequently for propagation 1300-2200Z
  Start of the strong 40M meter European opening at ~2000Z
  Look for short 15 and 20 meter JA openings 2130-2300Z