## Slide 1: Antenna/Tower Reliability Tim Jellison W3YQ/KL7WV

## Slide 2
Use quality materials (don’t be a cheap ham!)
Do it right the first time
Perform regular inspections
Be safe when working on antennas and towers
Is it K3LR approved?

## Slide 4: Use only good quality materials
Name-brand connectors only

## Slide 5: Use only good quality materials
Consider pre-made cables

## Slide 6: Use only good quality materials
Only use good quality tape

## Slide 7
Moisture is coax’s worst enemy. All outdoor connections must be properly sealed. Here’s a proven method to keep connections dry.

## Slide 8: Weatherproofing connections
First, tighten with pliers. Finger-tight is not good enough.

## Slide 9: Weatherproofing connections
One wrap of 88 tape. And always cut the end when taping. Never pull/tear the end or you’ll end up with a tail.

## Slide 10: Weatherproofing connections
Add a layer of mastic.

## Slide 11: Weatherproofing connections

## Slide 12: Weatherproofing connections
Two wraps of 88 tape. Overlap each layer by ½ the width of the tape.

## Slide 13
There are two tips in the next photo.
First, tape your cables with 88 tape – no tiewraps. Tiewraps can smash the coax and they will eventually fail due to weathering.
Second, always put a barrel at the top of your tower if the feedpoint is out of reach. Makes antenna removal much easier.

## Slide 15: Use a piece of split loom if there’s a concern about cables rubbing.

## Slide 16: Waterproofing a bearing
Does your antenna sometimes not turn in the cold weather? It might be ice in your thrust bearing. Make a boot out of one of these.

## Slide 17: Waterproofing a bearing

## Slide 18
It can also keep the water out of an Orion 2800’s top bearing.

## Slide 19
The bolts in a TB3 can seize up. Apply anti-seize before installation or swap out the bolts with stainless (and maybe still use anti-seize?)

## Slide 21
Notice all the blue stuff? You should also use a lubricant on all stainless hardware. Blue Locktite is a good choice. It lubricates, locks, yet can still be removed later.

## Slide 22
Also, when installing a Rohn tower, use anti-seize on the leg joints. It’s conductive and makes the inevitable disassembly much easier.

## Slide 23
Tidbits

## Slide 24
Does your rotor or antenna slip on the mast? You can add a secondary clamp which will help out your U-bolts.

## Slide 25: Here we give a Yaesu rotor some help

## Slide 26: Here is a secondary clamp below the mast clamp of a 40M Yagi

## Slide 27
If the top section of your tower is above the top set of guys, the leg bolts MUST be tight and should be regularly checked. This is a point of great lateral stress and if the bolts loosen, the holes in the legs will elongate.

## Slide 29
Do not over tighten anything on a Rohn tower leg. You could smash the leg (it can even split) and the tower will be compromised.

## Slide 31
When soldering PL259’s, don’t be afraid to use a big iron and get the connector hot – the solder must flow. Just keep everything straight in-line and be sure to let it cool down completely before you move it. That way the center dielectric will harden back up. I let mine sit about 10 minutes after soldering before doing anything with it.

## Slide 33
Solder all your crimps, otherwise the wire could pull out. If you’re using insulated lugs, don’t worry about melting the plastic.

## Slide 34: Conductive paste
Usable on all metal to metal joints, especially aluminum antenna joints.

## Slide 35: And above all, when climbing follow all safety rules!
NO SK’s